RYK-9107 Pro Portable Security Recorder (2.5" LCD) Features：

Built-in camera with 6 pieces IR LED. 2.5" LCD panel for instant view Remote controller of the system. Rechargeable battery for mobile usage. Able to power the external cameras. Stores images as ASF file format in SD card and can be downloaded to PC via USB connection. Recording mode: manual / continuous / motion detection / alarm. Audio record and playback using internal microphone, speaker and earphone. Multi-language OSD: English, Tradition Chinese, German, Spanish, Italian, French and Japanese.

Instruction :

REC: Red LED light indicates recording / Green LED light indicates power-on. Red LED Flash * SD card storage capacity is full or Error. *Continuous Flash : Recording. Abnormal Operation Warning: When LED is flashing quickly ,press«Enter» button to disable the alarm. CHG Power charging LED indicator ,lights on when charging and off when charging is complete. F Function button. F+IR Button switch [ IR ON / OFF ]. F+LCD Button switch [ON / OFF status bar], [Display OFF], and [Display ON]. During monitoring to playback.；During playback to pause.；During pause to return to playback. Stop recording or exit. Manual recording. Power Input (DC 5V/1A.) SD Card Slot. (SD card storage connection.) ▲/▼/◄/► Key 4Direction button(▲/▼/◄/►)and central button(Confirm / Menu). ▲and▼Key During menu setup to move the cursor Up / Down the item list. During playback to Increase / Decrease the speaker volume. ◄and►Key During menu setup to Increase / Decrease the setup value. During playback to Fast Rewind / Fast Forward. During pause to Step Rewind / Step Forward. Central Button(Confirm) During menu setup to enter submenu or to confirm setup. Central Button (Menu) During monitoring to enter setup. Speaker：Sound output. Monitor：Display video images (purchase separately). Earphone In：Earphone audio connection. AV IN：Video/Audio input connection. AV OUT Video/Audio output connection. Microphone Audio recording. IR Illuminator Night illumination function (purchase separately). Camera Connect to camera to view image (purchase separately). Control all function buttons Control all function buttons (Button Effective / Button Ineffective). Power Power button (ON / OFF).

Storage Capacity : Quality Level 640x480@12 IPS 320x240@30 IPS High 155 150 Medium 280 380 Low 340 600 (Approx for recording motion movie with 1GB Card.) Specifications : Model Name RYK-9107 Video System NTSC / PAL with Video Loss Auto Detection Video Codec MPEG4-SP ASF File Format Video Recording Frame Rate Max. 320x240@30 IPS / 640x480@12 IPS Video Recording Quality High / Medium / Low Video Recording Mode Manual / Schedule ( Alarm / Motion Detection / Continuous) Video Time Stamp Overlay with Video Images in ASF File Audio Input：1CH, Phone Jack / Audio Output：1CH, Phone Jack Motion Detection Setting Multiple Blocks and adjustable sensitivity Event Search Function Property and first image of selected file is displayed Playback Function Play / Fast Forward / Fast Rewind / Pause / Step Forward / Step Rewind Playback Speed x1 / x2 / x4 / x8 / x16 / x32 Power Supply DC5V / 1A, Rechargeable Li-ion Battery Storage Media：Secure Digital (SD) Card / Serial Port：USB 1.1 (Read-Only) Video Input：1CH, Phone Jack / Video Output：1CH, Phone Jack Audio Sampling Rate：44.1 KHz / Audio Codec：G.726 / 32 kbps Audio Device：Microphone / Speaker / Earphone Weight：175g / Dimensions( W x H x D )：86 x 55 x 22.5 mm Operating Environment：30 ~ 80% RH, 5°C ~ 40°C (41°F ~ 104°F) Optional Function：Camera / Remote Control / LCD / Camera Sensor：1/6" Color CMOS Sensor Camera Effective Picture：VGA (H/V: 640x480) / Camera S/N Ratio：46dB Camera Lens：Cone Lens 3.62mm / F2.8 / Camera Infrared Luminary：6 pieces IR-LED Camera Infrared Wavelength：850nm / Camera Infrared Illumination：5 M Remote Control：2.4GHz Transmission / LCD：2.5" Color TFT-LCD *Design and specifications are subject to change without notice.

Meicheng® MEI CHENG AUDIO VIDEO CO., LTD.

Address:13F, No. 2, Jian 8th Rd., Jhonghe City, Taipei County 23511, TAIWAN Tel: +886(2) 8228 0311, Fax: +886(2) 8228 0319 Website: www.meicheng.com.tw Email:mei.cheng@msa.hinet.net

# Text boxes

Meicheng

®

www.meicheng.com.tw

Pro Portable Security Recorder (2.5" LCD)  RYK-9107

▼Car camera / recorder